## Slide 1: Lecture 19 Unit II:ALU Design
Prepared By:
AVITA KATAL
Assistant Professor
Department of Virtualization
SoCSE

## Slide 2: Contents
1.Major hazards in pipelined execution
1.1. Structural hazards
1.2. Data hazards
1.3. Control hazards
2. RISC pipeline

## Slide 3: 1. Major Hazards in a Pipelined Execution
  Structural hazards(Resource Conflicts)
  Hardware Resources required by the instructions in
  simultaneous overlapped execution cannot be met
  Data hazards (Data Dependency Conflicts)
  An instruction scheduled to be executed in the pipeline requires the
  result of a previous instruction, which is not yet available
JMP
ID
PC
+
PC
bubble
IF
ID
OF
OE
OS
Branch address dependency
Hazards in pipelines may make it
necessary to stall the pipeline
Pipeline Interlock:
Detect Hazards Stall until it is cleared
ADD
DA
B,C
+
INC
DA
+1
R1
bubble
Data dependency
  R1 <- B + C
  R1 <- R1 + 1
  Control hazards (Branch conflicts)
  Branches and other instructions that change the PC
  make the fetch of the next instruction to be delayed

## Slide 4: 1.1. Structural Hazards
Structural Hazards
Occur when some resource has not been
duplicated enough to allow all combinations
of instructions in the pipeline to execute
Example: With one memory-port, a data and an instruction fetch
cannot be initiated in the same clock
The Pipeline is stalled for a structural hazard
<- Two Loads with one port memory
-> Two-port memory will serve without stall
FI
DA
FO
EX
i
i+1
i+2
FI
DA
FO
EX
FI
DA
FO
EX
stall
stall

## Slide 5: 1.2. Data Hazards
Data Hazards
Occurs when the execution of an instruction
depends on the results of a previous instruction
ADD R1, R2, R3
SUB R4, R1, R5
Hardware Technique
Interlock
- hardware detects the data dependencies and delays the scheduling
of the dependent instruction by stalling enough clock cycles
Forwarding (bypassing, short-circuiting)
- Accomplished by a data path that routes a value from a source
(usually an ALU) to a user, bypassing a designated register. This
allows the value to be produced to be used at an earlier stage in the
pipeline than would otherwise be possible
Software Technique
Instruction Scheduling(compiler) for delayed load
Data hazard can be dealt with either hardware
techniques or software technique

## Slide 6: 1.2.1 Forwarding Hardware
Register
file
Result
write bus
Bypass
path
ALU result buffer
MUX
ALU
R4
MUX
Example:
ADD R1, R2, R3
SUB R4, R1, R5
3-stage Pipeline
I: Instruction Fetch
A: Decode, Read Registers,
ALU Operations
E: Write the result to the destination register
I
A
E
ADD
SUB
I
A
E
Without Bypassing
I
A
E
SUB
With Bypassing

## Slide 7: 1. 2.2 Instruction Scheduling
a = b + c;
d = e - f;
Unscheduled code:
Delayed Load
A load requiring that the following instruction not use its result
Scheduled Code:
LW Rb, b
LW Rc, c
LW Re, e
ADD Ra, Rb, Rc
LW Rf, f
SW a, Ra
SUB Rd, Re, Rf
SW d, Rd
LW Rb, b
LW Rc, c
ADD Ra, Rb, Rc
SW a, Ra
LW Re, e
LW Rf, f
SUB Rd, Re, Rf
SW d, Rd

## Slide 8: 1.3 Control Hazards
Branch Instructions
- Branch target address is not known until
the branch instruction is completed
- Stall -> waste of cycle times
FI DA FO EX
FI DA FO EX
Branch
Instruction
Next
Instruction
Target address available
Dealing with Control Hazards
* Prefetch Target Instruction
* Branch Target Buffer
* Loop Buffer
* Branch Prediction
* Delayed Branch

## Slide 9: 1.3.1 Handling Control hazards
Prefetch Target Instruction
  Fetch instructions in both streams, branch not taken and branch taken
  Both are saved until branch branch is executed. Then, select the right
  instruction stream and discard the wrong stream
Branch Target Buffer(BTB; Associative Memory)
  Entry: Addr of previously executed branches; Target instruction
  and the next few instructions
  When fetching an instruction, search BTB.
  If found, fetch the instruction stream in BTB;
  If not, new stream is fetched and update BTB
Loop Buffer(High Speed Register file)
  Storage of entire loop that allows to execute a loop without accessing memory
Branch Prediction
  Guessing the branch condition, and fetch an instruction stream based on
  the guess. Correct guess eliminates the branch penalty
Delayed Branch
  Compiler detects the branch and rearranges the instruction sequence
  by inserting useful instructions that keep the pipeline busy
  in the presence of a branch instruction

## Slide 10: 2. RISC Pipeline
Instruction Cycles of Three-Stage Instruction Pipeline
RISC
- Machine with a very fast clock cycle that executes at the rate of one instruction per cycle
-> Simple Instruction Set
->Fixed Length Instruction Format
->Register-to-Register Operations
Data Manipulation Instructions
I: Instruction Fetch
A: Decode, Read Registers, ALU Operations
E: Write a Register
Load and Store Instructions
I: Instruction Fetch
A: Decode, Evaluate Effective Address
E: Register-to-Memory or Memory-to-Register
Program Control Instructions
I: Instruction Fetch
A: Decode, Evaluate Branch Address
E: Write Register(PC)

## Slide 11: 9.1 Delayed Load
Three-segment pipeline timing
Pipeline timing with data conflict
clock cycle 1 2 3 4 5 6
Load R1 I A E
Load R2 I A E
Add R1+R2 I A E
Store R3 I A E
Pipeline timing with delayed load
clock cycle 1 2 3 4 5 6 7
Load R1 I A E
Load R2 I A E
NOP I A E
Add R1+R2 I A E
Store R3 I A E
  LOAD: R1  M[address 1]
  LOAD: R2  M[address 2]
  ADD: R3  R1 + R2
  STORE: M[address 3]  R3
The data dependency is taken
care by the compiler rather
than the hardware

## Slide 12: 9.2 Delayed Branch
Compiler analyzes the instructions before and after
the branch and rearranges the program sequence by
inserting useful instructions in the delay steps
Using no-operation instructions
Rearranging the instructions

## Slide 13: Thanks