## Slide 1: INPUT/OUTPUT ORGANIZATION
Accessing I/O Devices
I/O interface
Input/output mechanism Memory-mapped I/O Programmed I/O
Interrupts
Direct Memory Access
Buses
Synchronous Bus Asynchronous Bus

## Slide 2: I/O in CO and O/S
Programmed I/O
Interrupts
•
DMA (Direct memory Access)

## Slide 3
A bus is a shared communication link, which uses one set of wires to connect multiple subsystems.
The two major advantages of the bus organization are versatility and low cost.

## Slide 4: Accessing I/O Devices
Most modern computers use single bus arrangement for connecting I/O devices to CPU & Memory
The bus enables all the devices connected to it to exchange information
Bus consists of 3 set of lines : Address, Data, Control
Processor places a particular address (unique for an I/O Dev.) on address lines
Device which recognizes this address responds to the commands issued on the Control lines
Processor requests for either Read / Write
The data will be placed on Data lines

## Slide 5: Hardware to connect I/O devices to bus
Interface Circuit
  Address Decoder
  Control Circuits
  Data registers
  Status registers
The Registers in I/O Interface – buffer and control
Flags in Status Registers, like SIN, SOUT
Data Registers, like Data-IN, Data-OUT

## Slide 6: I/O interface for an input device
Memory
Processor
Address
Data Control
I/O
Address
Decoders
Control
circuits
Data and status
registers
Interface
Input device (s)