## Slide 1: Section 2 – Storage Systems Architecture
Introduction

## Slide 2: Section Objectives
Upon completion of this Section, you will be able to:
Describe the host environment.
Describe common connectivity components and protocols.
Describe features of intelligent disk subsystems.
Describe data flow from the host to/from the disk.

## Slide 3: In this Section …
This section contains the following modules:
The Host Environment
Connectivity
Physical Disks
RAID Arrays
Storage Systems

## Slide 4: Storage System Environment
Storage System environments have evolved along with the changes in computing models. Storage has evolved from single internal disks to storage systems.
A storage system is a group of components that provide storage to one or more computers. The storage system is responsible for both the requests (commands) to read/write data as well as the actual transmission of the data.
At a very high level, a storage system includes:
Host system – Interact with the operating system and applications that require data.
Connectivity – Carries read/write commands and the data between the host and the storage devices.
Storage System – Devices where the data is stored.
Notes: Storage System environments have evolved along with the changes in computing models. Storage has evolved from single internal disks to storage systems. A storage system is a group of components that provide storage to one or more computers. The storage system is responsible for both the requests (commands) to read/write data as well as the actual transmission of the data. At a very high level, a storage system includes:
Host system – Interact with the operating system and applications that require data.
Connectivity – Carries read/write commands and the data between the host and the storage devices.
Storage System – Devices where the data is stored.
The modules in this section look in detail at each of these parts of the storage system environment.
Host
Connectivity
Storage

## Slide 5: Parts of a Storage Environment: Host
The process of storing data is distributed across many parts of a storage system. From the host’s perspective, storage access (read and write) occurs via
Physical components:
  CPU
  Memory
  Bus
Logical components:
  Software applications
  Operating system
  File systems
  Databases.
Notes: The process of storing data is distributed across many parts of a storage system. From the host’s perspective, storage access (read and write) occurs via
Physical components:
  CPU
  Memory
  Bus
Logical components:
  Software applications
  Operating system
  File systems
  Databases.
Host

## Slide 6: Parts of a Storage Environment: Connectivity
Network Connectivity encompasses everything between the host and the storage system.
Physical components of Connectivity include:
Wiring
  Host internal bus
  Cables – Optical and Copper
  Connectors and plugs
Adapters
  Host Bus Adapter (HBA) – enables devices to connect to a host’s internal bus system.
  Network Interface Cards – enables simple network attachments to a host.
Switches/hubs
  Manage traffic within a network. Logical components of Connectivity include : Communication protocols Device Drivers
Notes: Network Connectivity encompasses everything between the host and the storage system.
Physical components of Connectivity include:
Wiring
  Host internal bus(es)
  Cables – Optical and Copper
  Connectors and plugs
Adapters
  Host Bus Adapter (HBA) – enables devices to connect to a host’s internal bus system.
  Network Interface Cards – enables simple network attachments to a host.
Switches/hubs
  Manage traffic within a network.
Logical components of Connectivity include
Communication protocols
Device Drivers
Connectivity

## Slide 7: Parts of a Storage Environment: Storage
Physical components of storage include:
Physical devices that hold the data (i.e., disk, tape, optical drives, etc.)
Components that make the devices operate (i.e., power supplies, fans)
The enclosures that hold the equipment (e.g., racks)
Logical components of storage include:
Protocols
Flow algorithms
Notes: Physical components of storage include:
Physical devices that hold the data (i.e., disk, tape, optical drives, etc.)
Components that make the devices operate (i.e., power supplies, fans)
The enclosures that hold the equipment (e.g., racks)
Logical components of storage include:
Protocols
Flow algorithms
Storage

## Slide 8: The Host Environment
Module 2.1

## Slide 9: The Host Environment
Upon completion of this module, you will be able to:
List the hardware and software components of the host environment
Describe key protocols and concepts used by each component
Notes: In most storage systems, the host makes requests for data to be read/written. In this module, we will look at the hardware and software components used in the host environment as well as the key protocols and concepts that make these components work. This will give you the context for how data typically flows within the environment.

## Slide 10: Examples of Hosts
Laptop
Server
Group of Servers
Mainframe
Notes: A host environment could be something small, like a laptop, or it could be larger, such as a server, a group of servers, a mainframe, or a combination of these items. The host system has hardware (physical) and software (logical) components. Let’s look at the hardware components first.

## Slide 11: Host Physical Components
Bus
I/O Devices
CPU
Storage
Notes: A host may be considered to consist of the following 3 hardware building blocks:
  Central Processing Unit (CPU)
  Storage such as internal memory or disk devices
  Input/Output (I/O) devices.
Each of the 3 building blocks is covered in more detail in subsequent slides. The bus, or communication pathway that joins the building blocks, is covered in a later module.

## Slide 12: CPU
CPU
Bus
Bus
ALU
Registers
L1 Cache
Notes: The CPU consists of 3 major parts –
  Arithmetic Logic Unit
  Registers – a collection of very high speed storage locations
  Level 1 (L1) cache – although cache is optional, it is found on most modern CPUs.
The CPU connects to other components in the host via a bus. See the Connectivity module for a discussion of buses.

## Slide 13: Storage
…
0
1
2
3
n
Data 0
Data n
Data 2
Data 3
Data 1
Address
Content
Disk
Memory
Notes: Host storage can be made up of silicon “chips” or magnetic/optical media.
Memory is an example of storage in chips. Generally, there are two types of memory within a host system:
  Random Access Memory (RAM), This is the most common form of memory. It allows direct access to any memory location and can have data written into it or read from it.
  Read Only Memory (ROM), that contains data that can be read, but not changed. It is usually used for data needed during internal routines such as starting up the system.
Modern hosts can make use of large amounts of memory – 16 GB and upwards.
Examples of media-based host storage include:
  Hard disk
  CDROM or DVDROM
  Floppy disk
  Tape drive

## Slide 14: Storage Hierarchy – Speed and Cost
Speed
Slow
Fast
Cost
High
Low
Tape
Optical disk
Magnetic disk
RAM
L2 cache
L1 cache
CPU registers
Notes: In any host system, there will be a variety of storage types and each type will have different characteristics of speed, cost and capacity. As a general rule, faster technologies cost more, and are more scarce as a result.
CPU registers are extremely fast, but limited in number to a few tens of locations at most, and are expensive in terms of both financial cost and power use. As we move down the list, speeds decrease along with cost.
Magnetic disk has the medium tied to the drive (in most modern drives), whereas optical disk and tape use removable media. The cost of the media per MB stored is much lower than that of magnetic disk.

## Slide 15: Storage Hierarchy – Speed and Cost
In any host system, there will be a variety of storage types and each type will have different characteristics of speed, cost and capacity. As a general rule, faster technologies cost more, and are more scarce as a result.
CPU registers are extremely fast, but limited in number to a few tens of locations at most, and are expensive in terms of both financial cost and power use. As we move down the list, speeds decrease along with cost.
Magnetic disk has the medium tied to the drive (in most modern drives), whereas optical disk and tape use removable media. The cost of the media per MB stored is much lower than that of magnetic disk.

## Slide 16: I/O Devices
Human interface
  Keyboard
  Mouse
  Monitor
Computer-computer interface
  Network Interface Card (NIC)
Computer-peripheral interface
  USB (Universal Serial Bus) port
  Host Bus Adapter (HBA)
Notes: I/O devices allow a host to interact with the outside world by sending and receiving data. The basic I/O devices, such as the keyboard, mouse and monitor, allow users to enter data and view the results of operations. Other I/O devices allow hosts to communicate with each other or with peripheral devices, such as printers and cameras.

## Slide 17: Host Environment: Logical Components
Notes: Host systems generally include software components:
  Applications - provide a point of interaction either between the user and the host or another system and the host. Most applications have storage requirements, which may be short or long-term depending upon the application.
  Operating system - controls all aspects of the computing environment. It manages the user interface and the internal operations of all hardware components of the system. The Operating System:
    Controls interaction between applications and the storage systems.
    Monitors and responds to user actions and the environment.
    Organizes and controls the hardware components
    Connects hardware components to the application program layer and the users.
    Manages system activities such as storage and communication.
  File System (and Files) - provides a logical structure for data and methods for accessing that data.
  Device drivers - allow the operating system to be aware of and use a standard interface to access and control a specific device (i.e., printer, speakers, mouse, keyboard, video, storage devices, etc.). They provide the appropriate protocols to the host to allow access to the device.

## Slide 18
The file system is the general name given to the host-based logical structures and software routines used to control access to data storage.
The file system block is the smallest ‘container’ allocated to a file’s data. Each filesystem block is a contiguous area of physical disk capacity.
  Blocks can range in size depending on the type of files being stored and accessed.
  The block size is fixed (by the operating system) at the time of storage system configuration.
  Since most files are larger than the pre-defined filesystem block size, a file’s data will span multiple filesystem blocks. However, the filesystem blocks containing all of the file’s data may not necessarily be contiguous on a physical disk.
The file organization structure is important to users when identifying information stored in files.
  Hosts work with data stored in blocks.
  The filesystem converts the user logical structures into host accessible blocks.

## Slide 19
In multi-user, multi-tasking environments, filesystems manage shared storage resources using:
  Directories, paths and structures to identify file locations
  Volume Managers to hide the complexity of physical disk structures
  File locking capabilities to control access and data flow to and from file locations when used by potentially competing users or applications
  Databases and data management components such as:
    Large, shared relational databases
    Management of shared data storage

## Slide 20: File Systems
Notes: The file system is the general name given to the host-based logical structures and software routines used to control access to data storage.
The file system block is the smallest ‘container’ allocated to a file’s data. Each filesystem block is a contiguous area of physical disk capacity.
  Blocks can range in size depending on the type of files being stored and accessed.
  The block size is fixed (by the operating system) at the time of storage system configuration.
  Since most files are larger than the pre-defined filesystem block size, a file’s data will span multiple filesystem blocks. However, the filesystem blocks containing all of the file’s data may not necessarily be contiguous on a physical disk.
The file organization structure is important to users when identifying information stored in files.
  Hosts work with data stored in blocks.
  The filesystem converts the user logical structures into host accessible blocks.
In multi-user, multi-tasking environments, filesystems manage shared storage resources using:
  Directories, paths and structures to identify file locations
  Volume Managers to hide the complexity of physical disk structures
  File locking capabilities to control access and data flow to and from file locations when used by potentially competing users or applications
  Databases and data management components such as:
    Large, shared relational databases
    Management of shared data storage

## Slide 21
The number of files on a system can be extensive and could quickly get out of hand. Instead of using a linear or flat structure (similar to having many objects in a single box), a filesystem will be divided into directories (smaller boxes), called folders in the Windows environment.
Directories:
  Organize file systems into containers which may hold files as well as other directories
  Hold information about files that they contain
A directory is really just a special type of file containing a list of filenames and associated metadata (information or data about the file). When a user attempts to access a given file by name, the name is used to look up the appropriate entry in the directory. That entry will hold the corresponding metadata.

## Slide 22: File Systems: Journaling and Logging
Improves data integrity and system restart time over non-journaling file systems.
Uses a separate area called a log or journal.
  May hold all data to be written
  May hold only metadata
Disadvantage - slower than other file systems.
  Each file system update requires at least 1 extra write – to the log
Notes: Non-journaling file systems create a potential for lost files because they may use many separate writes to update their data and metadata. If the system crashes during the write process, metadata or data may be lost or corrupted. When the system reboots, the filesystem will attempt to update the metadata structures by examining and repairing them. This operation takes a long time on large file systems. If there is insufficient information to recreate the desired or original structure, files may be misplaced or lost.
A journaling file system uses a separate area called a log, or journal. This journal may contain all the data to be written (physical journal), or may contain only the metadata to be updated (logical journal). Before changes are made to the filesystem, they are written to this separate area. Once the journal has been updated, the operation on the filesystem can be performed. If the system crashes during the operation, there is enough information in the log to "replay" the log record and complete the operation.
Journaling results in a very quick filesystem check by only looking at the active, most recently accessed parts of a large file system. In addition, because information about the pending operation is saved, the risk of files being lost is lessened.
A disadvantage of journaling filesystems is that they are slower than other file systems. This slowdown is the result of the extra operations that have to be performed on the journal each time the filesystem is changed.

## Slide 23
Non-journaling file systems create a potential for lost files because they may use many separate writes to update their data and metadata.
If the system crashes during the write process, metadata or data may be lost or corrupted. When the system reboots, the filesystem will attempt to update the metadata structures by examining and repairing them. This operation takes a long time on large file systems.
If there is insufficient information to recreate the desired or original structure, files may be misplaced or lost.

## Slide 24
A journaling file system uses a separate area called a log, or journal. This journal may contain all the data to be written (physical journal), or may contain only the metadata to be updated (logical journal). Before changes are made to the filesystem, they are written to this separate area. Once the journal has been updated, the operation on the filesystem can be performed. If the system crashes during the operation, there is enough information in the log to "replay" the log record and complete the operation.
Journaling results in a very quick filesystem check by only looking at the active, most recently accessed parts of a large file system. In addition, because information about the pending operation is saved, the risk of files being lost is lessened.
A disadvantage of journaling filesystems is that they are slower than other file systems. This slowdown is the result of the extra operations that have to be performed on the journal each time the filesystem is changed.

## Slide 25: Volume Management
Notes: The Volume Manager is an optional intermediate layer between the filesystem and the physical disks. It can aggregate several smaller disks to form a larger virtual disk and make this virtual disk visible to higher level programs and applications. It optimizes access to storage and simplifies the management of storage resources.

## Slide 26: Volume Management
The Volume Manager is an optional intermediate layer between the filesystem and the physical disks. It can aggregate several smaller disks to form a larger virtual disk and make this virtual disk visible to higher level programs and applications. It optimizes access to storage and simplifies the management of storage resources.

## Slide 27: HBAs
Notes: The host connects to storage devices using special hardware called a Host Bus Adapter (HBA). HBAs are generally implemented as either an add-on card or a chip on the motherboard of the host. The ports on the HBA are the host’s connection to the storage subsystem. There may be multiple HBAs in a host.
The HBA has the processing capability to handle some storage commands, thereby reducing the burden on the host CPU.

## Slide 28: HBAs
The host connects to storage devices using special hardware called a Host Bus Adapter (HBA). HBAs are generally implemented as either an add-on card or a chip on the motherboard of the host. The ports on the HBA are the host’s connection to the storage subsystem. There may be multiple HBAs in a host.
The HBA has the processing capability to handle some storage commands, thereby reducing the burden on the host CPU.

## Slide 29: Improving Data Availability at the Host
Redundancy:
Multiple HBAs
Multi-pathing software
Clustering
Notes: Large computing environments usually need uninterrupted access to their critical data. Hosts can be configured to support this need through:
  Redundancy can be implemented using multiple HBAs. HBAs are the host’s connection to the storage subsystem.
  Multi-pathing software is a server-resident, availability enhancing, software solution. It utilizes the available HBAs on the server to provide redundant communication paths between host and storage devices. It provides multiple path I/O capabilities and path failover, and may also provide automatic load balancing. This assures uninterrupted data transfers even in the event of a path failure.
  Clustering uses redundant host systems connected together. In the event that one of the hosts in the cluster fails, its functions will be assumed by the surviving member(s). Cluster members can be configured to transparently take over each others’ workload, with minimal or no impact to the user.

## Slide 30: Module Summary
Key points covered in this module:
Hosts typically have:
  Hardware: CPU, memory, buses, disks, ports, and interfaces.
  Software: applications, operating systems, file systems, device drivers, volume managers
HBAs connect hosts to storage devices.
Multi-pathing software uses redundant paths to ensure uninterrupted communication between the host and the storage
Clustering uses redundant host systems to improve data availability

## Slide 31: Check Your Knowledge
What are some examples of hosts?
Describe the hardware components found in most hosts.
What is the function of the operating system?
What is the function of the file system?
What are some techniques that can be used to improve availability at the host?
What is volume management?


## Slide 32: Connectivity
Module 2.2

## Slide 33: Connectivity
Upon completion of this module, you will be able to:
Describe the physical components of a networked storage environment.
Describe the logical components (communication protocols) of a networked storage environment.
Notes: In the previous module, we looked at the host environment. In this module, we will look at how the host is connected to storage, and the logical protocols used for communication between them.

## Slide 34: Physical Components – Host with Internal Storage
Bus
Disk
Cable
Host
Port
Port
HBA
CPU
Notes: There are three key connectivity components associated with host systems:
Bus – for example, connecting the CPU to memory.
Ports – connections to external devices such as printers, scanners, or storage.
Cables – copper or fiber optic “wires” connecting a host to external devices.
A host with internal storage may be anything from a laptop to a large enterprise server. All of the components are internal to the host enclosure; we’ll look at the bus, port and cable in more detail.

## Slide 35: Bus Technology
Serial
Serial Bi-directional
Parallel
Notes: A bus is a collection of paths that facilitate data transmission from one part of the computer to another.
Physical components communicate across a bus by sending packages of data between the devices. These packets can travel in a serial path or in parallel paths. In serial communication, the bits travel one behind the other. In parallel communication, the bits can move along redundant paths simultaneously.

## Slide 36: Bus Technology
System Bus – connects CPU to Memory
Local (I/O) Bus – carries data to/from peripheral devices.
Bus width measured in bits
Bus speed measured in MHz
Throughput measured in MB/S
Notes: Generally, there are at least two types of buses in a computer system:
  System Bus – that carries data from the processor to memory, and
  Local or I/O Bus – that carries data to/from peripheral devices such as storage devices. The local bus is a high-speed pathway that connects directly to the processor.
The size of a bus, known as its width, is important because it determines how much data can be transmitted at one time. For example, a 16-bit bus can transmit 16 bits of data, whereas a 32-bit bus can transmit 32 bits of data. The width of a bus may be compared to the number of lanes on a highway.
Every bus has a clock speed measured in MHz. A fast bus allows data to be transferred faster, which makes applications run faster.

## Slide 37: Connectivity Protocols
Protocol = a defined format for communication – allows the sending and receiving devices to agree on what is being communicated.
Tightly Connected Entities
Directly Attached Entities
Network Connected Entities
Notes: Protocol is a defined format, in this case for communication between hardware or software components.
  Communication protocols are defined for systems and components that are:
  Tightly connected entities – such as central processor to RAM, or storage buffers to controllers – use standard BUS technology (e.g. System bus or I/O – Local Bus).
  Directly attached entities are devices connected at moderate distances – such as host to printer or host to storage (JBOD or Direct Attached Storage (DAS))
  Network connected entities – such as networked hosts, Network Attached Storage (NAS) or Storage Area Networks (SAN)
We will discuss the communication protocols (logical components) found in each of these connectivity models. Let’s start with the tightly connected or bus protocols.

## Slide 38: Communication Protocols
Host
Apps
Operating System
PCI
SCSI or IDE/ATA Device Drivers
Notes: The protocols for the local (I/O) bus and for connections to an internal disk system include:
  PCI
  IDE/ATA
  SCSI
Let’s look at each.

## Slide 39: Bus Technology - PCI
Peripheral Component Interconnect (PCI) defines the local bus system within a computer
It is an interconnection between microprocessor and attached devices, in which expansion slots are spaced closely for high-speed operation.
Has Plug and Play functionality.
PCI is 32/64 bit
Throughput is 133 MB/sec
Notes: The Peripheral Component Interconnect (PCI) is a specification defining the local bus system within a computer. The specification standardizes how PCI expansion cards, such as network cards or modems, install themselves and exchange information with the central processing unit (CPU).
In more detail, a Peripheral Component Interconnect (PCI) includes:
  an interconnection system between a microprocessor and attached devices, in which expansion slots are spaced closely for high-speed operation.
  plug and play functionality that makes it easy for a host to recognize a new card
  32 or 64 bit data
  a throughput of 133 MB/sec.
PCI Express is an enhanced PCI bus with increased bandwidth.

## Slide 40: IDE/ATA
Integrated Device Electronics (IDE) / Advanced Technology Attachment (ATA)
Most popular interface used with modern hard disks
Good performance at low cost
Desktop and laptop systems
Inexpensive storage interconnect
Notes: The most popular interface protocol used in modern hard disks is the one most commonly known as IDE. This interface is also known as ATA.
IDE/ATA hard disks are used in most modern PCs, and offer excellent performance at relatively low cost.

## Slide 41: SCSI - Small Computer System Interface
Most popular hard disk interface for servers.
Higher cost than IDE/ATA.
Supports multiple simultaneous data access.
Currently both parallel and serial forms.
Used primarily in “higher end” environments.
Notes: Small Computer Systems Interface (SCSI)
The second-most popular hard disk interface protocol used in PCs today is SCSI. It has several advantages over IDE that make it preferable for many situations such as in higher-end machines. It is far less commonly used than IDE/ATA, due to its higher cost and the fact that its advantages are not useful for the typical home, or business desktop user.
It's important to remember that SCSI is a system interface. SCSI began as a parallel interface, allowing the connection of devices to a PC, or other systems, with data being transmitted across multiple data lines. SCSI itself, however, has been broadened greatly in terms of its scope, and now includes a wide variety of related technologies and standards.

## Slide 42: SCSI Model
Target
Initiator
A SCSI device that starts a communication is an initiator.
A SCSI device that services a request is a target.
Note: If the initiator is a host, it will release the communication connection and continue processing other events while the target (usually a slower mechanical disk) executes the command. The host will await an interrupt signal from the storage device to complete the transaction.
Notes: A SCSI device that starts a communication is an initiator.
A SCSI device that services a request is a target.
Note: If the initiator is a host, it will release the communication connection and continue processing other events while the target (usually a slower mechanical disk) executes the command. The host will await an interrupt signal from the storage device to complete the transaction.

## Slide 43: SCSI Model
Target ID
Initiator ID
LUNs
Components of a SCSI communication include:
  Initiator ID – uniquely identifies an initiator that is used as an “originating address”.
  Target ID – uniquely identifies a target. Used as the address for exchanging commands and status information with initiators.
  Logical Unit Numbers (LUNs) – identifies a specific Logical Unit in a target. Logical Units can be more than a single disk.
Notes: Components of a SCSI communication include:
  Initiator ID – uniquely identifies an initiator that is used as an “originating address”.
  Target ID – uniquely identifies a target. Used as the address for exchanging commands and status information with initiators.
  Logical Unit Numbers (LUNs) – identifies a specific Logical Unit in a target. Logical Units can be more than a single disk.

## Slide 44: SCSI Addressing
Initiator ID - a number from 0 to 15 with the most common value being 7.
Target ID - a number from 0 to 15
LUN - a number that specifies a device addressable through a target.
Initiator ID
Target ID
LUN
Notes:   Initiator ID = the original initiator ID number (used to send responses back to the initiator from the storage device). A SCSI host bus adapter (referred to as a controller) can be implemented in two ways:
    An onboard interface or
    An ‘add in’ card plugged into the system I/O bus.
  Target ID = Value for a specific storage device. An address that is set on the interface of the device such as a disk, tape or CDROM.
  LUN = Logical Unit Number of the device – reflects the actual address of the device, as seen by the target.

## Slide 45: Disk Identifier - Addressing
c0 - Controller Initiator, HBA
Peripheral Controller
t0
Target
LUNs
d0
d1
d2
Host Addressing
  Controller
  Target
  LUN
c0 t0 d0
Notes: For example, a logical device name (used by a host) for a disk drive may be: cn|tn|dn where
  cn is the controller
  tn is the target ID of the devices such as t0, t1, t2 and so on
  dn is the device number, which reflects the actual address of the device unit. This is usually d0 for most SCSI disks because there is only one disk attached to the target controller. In intelligent storage systems, discussed later, each target may address many LUNs.

## Slide 46: SCSI - Pros and Cons
Pros:
  Fast transfer speeds, up to 320 megabytes per second
  Reliable, durable components
  Can connect many devices with a single bus, more than just HDs
  SCSI host cards can be put in almost any system
  Full backwards compatibility
Cons:
  Configuration and setup specific to one computer
  Unlike IDE, few BIOS support the standard
  Overwhelming number of variations in the standard, hardware, and connectors
  No common software interfaces and protocol
Notes: SCSI has many significant advantages in relation to IDE. SCSI
  Has a faster transfer speed (Note: 320 MB/s refers to parallel SCSI. Serial SCSI may be different.)
  Has robust software and hardware
  Can connect many devices to a computer
  Allows SCSI Host Adapter cards to be put into almost any system, and
  SCSI supports a remarkable level of backwards compatibility.

## Slide 47: Comparison IDE/ATA vs SCSI
Feature
IDE/ATA
SCSI
Connectivity Market
Internal Storage
Internal and External Storage
Speed (MB/sec)
100/133/150
320
Hot Pluggable
No
Yes
Expandability
Easier to set up
Very good but very expensive to set up
Cost/Performance
Good
High cost/Fast transfer speed
Notes: Expandability and Number of Devices, SCSI is superior to IDE/ATA. This advantage of SCSI only matters if you actually need this much expansion capability, because SCSI is more involved and expensive to set up.
Device Type Support – SCSI holds a significant advantage over IDE/ATA in terms of the types of devices each interface supports.
Cost – the IDE/ATA interface is superior to the SCSI interface.
Performance – These factors influence system performance for both interfaces:
  Maximum Interface Data Transfer Rate: Both interfaces presently offer very high maximum interface rates, so this is not an issue for most PC users. However, if you are using many hard disks at once, for example in a RAID array, SCSI will offer better overall performance.
  Device-Mixing Issues: IDE/ATA channels that mix hard disks and CD-ROMs are subject to significant performance hits due to the fact that these devices are operating at different speeds (hard disks read and write relatively quickly when compared to CDROM drives) and the IDE channel that can only support a single device at a time, must wait for the slower Optical drive to complete a task. SCSI does not have this problem.
  Device Performance: When looking at particular devices, SCSI can support multiple devices simultaneously while IDE/ATA can only support a single device at a time.
Configuration and set-up – IDE/ATA is easier to set up, especially if you are using a reasonably new machine and only a few devices. SCSI has a significant advantage over IDE/ATA in terms of hard disk addressing issues.

## Slide 48: Physical Components – Host with External Storage
Bus
Disk
Cable
Host
Port
Port
HBA
CPU
Notes: A host with external storage is usually a large enterprise server. Most of the components are internal to the host enclosure, though the cable and disk(s) will be external. Components are identical to those of a host with internal storage.
.

## Slide 49: Fibre Channel
Fibre Channel
Storage Arrays
Host
Apps
DBMS
Mgmt Utils
File System
LVM
Multipathing Software
Device Drivers
HBA
HBA
HBA
Notes: Fibre Channel is a high–speed interconnect used in networked storage to connect servers to shared storage devices. Fibre Channel components include HBAs, hubs, switches, cabling., and disks.
The term Fibre Channel refers to both the hardware components and the storage protocol that communicates across the channel elements.

## Slide 50: External Storage Interfaces – A Comparison
SCSI
  Limited distance
  Limited device count
  Usually limited to single initiator
  Single-ported drives
Fibre Channel
  Greater distance
  High device count in SANs
  Multiple initiators
  Dual-ported drives
Notes: The 2 most popular interfaces for external storage devices are SCSI and Fibre Channel (FC). SCSI is also commonly used for internal storage in hosts; FC is almost never used internally.

## Slide 51: Fibre Channel Connectivity
Switches
Storage
Hosts
Notes: When computing environments require high speed connectivity, they use sophisticated equipment to connect hosts to storage devices.
Physical connectivity components in networked storage environments include:
  HBA (Host-side interface) – Host Bus Adapters connect the host to the storage devices.
  Optical cables – fiber optic cables to increase distance, and reduce cable bulk.
  Switches – used to control access to multiple attached devices
  Directors – sophisticated switches with high availability components
  Bridges – connections to different parts of a network.

## Slide 52
When computing environments require high speed connectivity, they use sophisticated equipment to connect hosts to storage devices.
Physical connectivity components in networked storage environments include:
  HBA (Host-side interface) – Host Bus Adapters connect the host to the storage devices.
  Optical cables – fiber optic cables to increase distance, and reduce cable bulk.
  Switches – used to control access to multiple attached devices
  Directors – sophisticated switches with high availability components
  Bridges – connections to different parts of a network.

## Slide 53: Module Summary
Key points covered in this module:
The physical components of a networked storage environment.
The logical components (communication protocols) of a networked storage environment.
Notes: We looked at how the host is connected to storage and the logical protocols of the communication between the two technology components.

## Slide 54: Check Your Knowledge
What are the key physical connectivity components of a small systems environment?
What are the key physical connectivity components of networked storage computing environments?
What are the key logical connectivity protocols found in all computing environments?


## Slide 55: Physical Disks
Module 2.3

## Slide 56: Physical Disks
After completing this module, you will be able to:
Describe the major physical components of a disk drive and their function
Define the logical constructs of a physical disk
Describe the access characteristics for disk drives and their performance implications
Describe the logical partitioning of physical drives
Notes: Reading and writing data is a vital component of storage system. There are several methods for storing data, however, in this module the focus will be on disk drives. Disk drives use many types of technology to perform their job: mechanical, chemical, magnetic, electrical. Our intent is not to make you an expert on every detail about the drive—rather you should have a high level understanding of how both the physical and logical parts of a drive work. This enables you to see how these parts impact system capacity, reliability, and performance.

## Slide 57: Lesson: Disk Drive Components
Upon completion of this lesson, you will be able to:
Describe the physical components of a disk drive
Describe the physical structure of a disk drive platter
Discuss how the geometry of a disk impacts how data is recorded on a platter
Differentiate between the logical organization of data and the physical organization on a disk drive
Notes: The focus of this lesson is on the components of a disk drive and how they work. Additionally, it is important to understand how the data is organized on the disk based on its disk geometry.

## Slide 58: Disk Drive Components: Platters
00110100111010101010
00110100111010101010
10110101011010101010
01010100111010101010
Notes: A hard drive contains a series of rotating platters within a sealed case. The sealed case is known as Head Disk Assembly, or HDA.
A platter has the following attributes:
  It is a rigid, round disk this is coated with magnetically sensitive material.
  Data is stored in binary code (0s and 1s). It is encoded by polarizing magnetic areas, or domains, on the disk surface.
  Data can be written to and read from both surfaces of a platter.
  A platter’s storage capacity varies across drives. There is an industry trend toward higher capacity as technology improves.
    Note: The drive’s capacity is determined by the number of platters, the amount of data which can be stored on each platter, and how efficiently data is written to the platter.
  The number of platters on a drive is specific to the particular drive.
Note: These concepts apply to disk drives used in systems of all sizes.

## Slide 59: Disk Drive Components: Spindle
Spindle
Platters
Notes: Multiple platters are connected by a spindle.
  The spindle is connected to a motor which rotates at a constant speed.
  The spindle rotates continuously until power is removed from the spindle motor.
  Many hard drive failures occur when the spindle motor fails.
Disk platters spin at speeds of several thousand revolutions per minute. These speeds will increase as technologies improve, though there is a physical limit to the extent to which they can improve.

## Slide 60: Disk Drive Components: Read/Write Heads
Notes: Data is read and written by read/write heads, or R/W heads. Most drives have two R/W heads per platter—one for each surface of the platter.
  When reading data they detect magnetic polarization on the platter surface.
  When writing data they change the magnetic polarization on the platter surface.
Since reading and writing data is a magnetic process, the R/W heads never actually touch the surface of the platter. There is a microscopic air gap between the read/write heads and the platter. This is known as the head flying height.
When the spindle rotation has stopped, the air gap is removed and the R/W heads rest on the surface of the platter in a special area near the spindle called a landing zone. The landing zone is coated with a lubricant to reduce head/platter friction. Logic on the disk drive ensures that the heads are moved to the landing zone before they touch the surface.
If the drive malfunctions and a read/write head accidentally touches the surface of the platter outside of the landing zone, it is called a head crash. When a head crash occurs, the magnetic coating on the platter gets scratched and damage may also occur to the R/W head. A head crash generally results in data loss.

## Slide 61: Disk Drive Components: Actuator
Actuator
Spindle
Notes: Read/write heads are mounted on the actuator arm assembly, which positions the read/write head at the location on the platter where data needs to be written or read.

## Slide 62: Physical Disk Structures: Actuator Arm Assembly
Actuator
R/W Head
R/W Head
Notes: The read/write heads for all of the platters in the drive in a drive are attached to one actuator arm assembly and move across the platter simultaneously. Notice that there are two read/write heads per platter, one for each surface.

## Slide 63: Disk Drive Components: Controller
Bottom View of Disk Drive
HDA
Controller
Interface
Power Connector
Notes: The controller is a printed circuit board, mounted at the bottom of the disk drive. It contains a microprocessor (as well as some internal memory, circuitry, and firmware) that controls:
  Power to the spindle motor and control of motor speed
  How the drive communicates with the CPU on the host system
  Reads/writes by moving the actuator arm, and switching between R/W heads
  Optimization of data access

## Slide 64: Physical Disk Structures: Sectors and Tracks
Sector
Track
Platter
Notes: Data is recorded in tracks. A track is a concentric ring around the spindle which contains information.
  A track can hold a large amount of information. Track density describes how tightly packed the tracks are on a platter.
  Tracks are numbered from the outer edge of the platter, starting at track zero.
  A track is divided into sectors. A sector is the smallest individually-addressable unit of storage.
  The number of sectors per track is based upon the specific drive.
  Sectors typically hold 512 bytes of user data. Some disks can be formatted with larger sectors.
  A formatting operation performed by the manufacturer writes the track and sector structure on the platter.
Each sector stores user data as well as other information, including its sector number, head number (or platter number) and track number. This information aids the controller in locating data on the drive, but it also takes up space on the disk. Thus there is a difference between the capacity of an unformatted disk and a formatted one. Drive manufacturers generally advertise the formatted capacity.
The first PC hard disks typically held 17 sectors per track. Today's hard disks can have a much larger number of sectors in a single track. There can be thousands of tracks on a platter, depending on the size of the drive.

## Slide 65: Platter Geometry and Zoned-Bit Recording
Platter Without Zones
Sector
Track
Platter With Zones
Notes: Since a platter is made up of concentric tracks, the outer tracks can hold more data than the inner ones because they are physically longer than the inner tracks. However, in older disk drives the outer tracks had the same number of sectors as the inner tracks, which means that the data density was very low on the outer tracks. This was an inefficient use of the available space.
Zoned-bit recording uses the disk more efficiently. It groups tracks into zones that are based upon their distance from the center of the disk. Each zone is assigned an appropriate number of sectors per track. This means that a zone near the center of the platter has fewer sectors per track than a zone on the outer edge.
In zoned-bit recording:
  Outside tracks have more sectors than inside tracks.
  Zones are numbered, with the outermost zone being Zone 0.
  Tracks within a given zone have the same number of sectors.
Note: The media transfer rate drops as the zones move closer to the center of the platter, meaning that performance is better on the zones created on the outside of the drive. Media transfer rate is covered later in the module.

## Slide 66: Physical Disk Structures: Cylinders
Cylinder
Tracks, Cylinders and Sectors
Notes: A cylinder is the set of identical tracks on both surfaces of each of the drive’s platters. Often the location of drive heads are referred to by cylinder number rather than by track number.

## Slide 67: Logical Block Addressing
Physical Address = CHS
Logical Block Address = Block #
Sector
Cylinder
Head
Block 0
Block 16
Block 32
Block 48
Block 8
(lower surface)
Notes: At one time, drives used physical addresses made up of the Cylinder, Head, and Sector number (CHS) to refer to specific locations on the disk. This meant that the host had to be aware of the geometry of each disk that was used.
Logical Block Addressing (LBA) simplifies addressing by a using a linear address for accessing physical blocks of data. The disk controller performs the translation process from LBA to CHS address. The host only needs to know the size of the disk drive (how many blocks).
  Logical blocks are mapped to physical sectors on a 1:1 basis.
  Block numbers start at 0 and increment by one until the last block is reached (E.g., 0, 1, 2, 3 … (N-1)).
  Block numbering starts at the beginning of a cylinder and continues until the end of that cylinder
  This is the traditional method for accessing peripherals on SCSI, Fibre Channel, and newer ATA disks.
  As an example, we’ll look at a new 500 GB drive. The true capacity of the drive is 465.7 GB, which is in excess of 976,000,000 blocks. Each block will have its own unique address.
In the slide, the drive shows 8 sectors per track, 8 heads, and 4 cylinders. We have a total of 8 x 8 x 4 = 256 blocks. The illustration on the right shows the block numbering, which will range from 0 to 255.

## Slide 68: What the Host Sees
A
One Logical Volume
Multiple Logical Volumes
A
B
C
D
Notes: Partitioning divides the disk into logical containers (known as volumes), each of which can be used for a particular purpose.
  Partitions are created from groups of contiguous cylinders
  A large physical drive could be partitioned into multiple Logical Volumes (LV) of smaller capacity.
  Several small physical drives can be concatenated together by a volume manager and presented as one logical volume.
  Partition size impacts disk space utilization
  The host filesystem accesses logical volumes, with no knowledge of the physical structure.
Note: Because partitions define the disk layout, they are generally created when the hard disk is initially set up on the host.

## Slide 69: Lesson Summary
Key points covered in this lesson:
Physical drives are made up of:
  HDA
    Platters connected via a spindle
    Read/write heads which are positioned by an actuator
  Controller
    Controls power, communication, positioning, and optimization
Data is structured on a drive using tracks, sectors, and cylinders
The geometry of a disk impacts how data is recorded on a platter

## Slide 70: Lesson: Disk Drive Performance
Upon completion of this lesson, you will be able to:
Describe the factors that impact the performance of a drive
Describe how drive reliability is measured
Notes: The focus of this lesson will be on the factors that impact how well a drive works, in particular, the performance and reliability of the drive.

## Slide 71: Disk Drive Performance: Positioning
Seek time is the time for read/write heads to move between tracks
Seek time specifications include:
  Full stroke
  Average
  Track-to-track
Notes: Seek times describes the time it takes to position the read/write heads radially across the platter. The following specifications are often published:
  Full Stroke - the time it takes to move across the entire width of the disk, from the innermost track to the outermost.
  Average – the average time it takes to move from one random track to another (normally listed as the time for one-third of a full stroke).
  Track-to-Track – the time it takes to move between adjacent tracks.
Each of these specifications is measured in milliseconds (ms).
Notes:
  Average seek times on modern disks will typically be in the range of 3 to 15 ms
  Seek time has more impact on reads of random tracks on the disk rather than on adjacent tracks.
  To improve seek time, data is often written only to a subset of the available cylinders (either on the inner or outer tracks), and the drive is treated as though it has a lower capacity than it really has, e.g. a 500 GB drive is set up to use only the first 40 % of the cylinders, and is treated as a 200 GB drive. This is known as short-stroking the drive.

## Slide 72: Disk Drive Performance: Rotational Speed/Latency
Notes: The actuator moves the read/write head over the platter to a particular track, while the platter spins to position the a particular sector under the read write head.
Rotational latency is the time that it takes the platter to rotate and position the data under the read/write head.
  Rotational latency is dependent upon the rotation speed of the spindle and is measured in milliseconds (ms)
  The average rotational latency is one-half of the time taken for a full rotation.
  Like seek times, rotational latency has more of an impact on reads or writes of random sectors on the disk than on the same operations on adjacent sectors.
Instructor note: rotational latency is around 5.5 ms for a 5,400 rpm drive, and around 2.0 ms for a 15,000 rpm drive.

## Slide 73: Disk Drive Performance: Command Queuing
Request 1
Request 2
Request 3
Request 4
1
2
3
4
Request 1
Request 2
Request 3
Request 4
1
3
2
4
Without Command Queuing
With Command Queuing
1
2
3
4
1
2
3
4
Notes: If commands are processed as they are received, time is wasted if the read/write head passes over data that will be needed one or two requests later. To improve drive performance, some drive manufacturers include logic that analyzes where data is stored on the platter relative to the data access requests. Requests are then reordered to make best use of the data’s layout on the disk.
This technique is known as Command Queuing (also known as Multiple Command Reordering, Multiple Command Optimization, Command Queuing and Reordering, Native Command Queuing or Tagged Command Queuing).
In addition to being performed at the physical disk level, command queuing can also be performed by the storage system that uses the disk. This will be discussed in the Storage Systems Overview module.

## Slide 74: Disk Drive Performance: Data Transfer Rate
Interface
Buffer
HBA
Disk Drive
Internal transfer rate measured here
External transfer rate measured here
Notes: The following steps take place when data is read from/written to the drive:
  Read
    Data moves from the disk platters to the heads
    Data moves from the heads to the drive's internal buffer
    Data moves from the buffer through the interface to the rest of the system, shown here as an HBA
  Write
    Data moves from the interface through the drive’s internal buffer.
    Data moves from the buffer to the read/write heads
    Data moves from the disk heads to the platters
The Data Transfer Rate describes the MB/second that the drive can deliver data to the HBA. Given that internal and external factors can impact performance transfer rates are refined to use:
  Internal transfer rate - the speed of moving data from the disk surface to the R/W heads on a single track of one surface of the disk. This is also known as the burst transfer rate.
    Sustained internal transfer rate takes other factors into account, such as seek times.
  External transfer rate - the rate at which data can be moved through the interface. The burst transfer rate is generally the advertised speed of the interface (E.g., 133 MB/s for ATA/133)
    Sustained external transfer rate will be lower than the interface speed.
Note: Internal transfer rates will almost always be lower, and sometimes appreciably lower, than the external transfer rate.

## Slide 75: Drive Reliability: MTBF
Mean Time Between Failure
Amount of time that one can anticipate a device to work before an incapacitating malfunction occurs
  Based on averages
  Measured in hours
Determined by artificially aging the product
Notes: Mean Time Between Failure (MTBF) is the amount of time that one can anticipate a device to work before an incapacitating malfunction occurs. It is based on averages and therefore is used merely to provide estimates. MTBF is measured in hours (e.g., 750,000 hours).
Note: MTBF is based on an aggregate analysis of a huge number of drives, so it does not help to determine how long a given drive will actually last. MTBF is often used along with the Service Life of the drive, which describes how long you can expect the drive’s components to work before they will wear out (E.g., 2 years).
Note: MTBF is a statistical method developed by the US Military as a way of estimating maintenance levels required by various devices. It is generally not practical to test a drive before it becomes available for sale (750,000 hours is over 85 years!). Instead, MTBF is tested by artificially aging the drives. This is accomplished by subjecting them to stressful environments such as high temperatures, high humidity, fluctuating voltages, etc.

## Slide 76: Lesson Summary
Key points covered in this lesson:
Drive performance is impacted by a number of factors including:
  Seek time
  Rotational latency
  Command queuing
  Data transfer rate
Drive reliability is measured using MTBF

## Slide 77: Module Summary
Key points covered in this module:
Physical drives are made up of a number of components
  HDA – houses the platters, spindles, actuator assemblies (which include the actuator and the read/write heads)
  Controller - Controls power, communication, positioning, and optimization
Data is structured on a drive using tracks, sectors, and cylinders
Drive performance is impacted by seek time, rotational latency, command queuing, and data transfer rate

## Slide 78: Check Your Knowledge
Describe the purpose of the actuator, the read/write head, and the controller on a drive.
What is the difference between a track, a sector, and a cylinder?
Why is zoned-bit recording used?
What is the difference between seek time and rotational latency?
What is the difference between internal and external data transfer rates?
What purpose does the MTBF specification serve?
