## Slide 1: Static and Dynamic Memory
Tanmay Bhowmik

## Slide 2: Dynamic RAM (DRAM)
Dynamic RAM, or DRAM is a form of random access memory, RAM. It is widely used in PCs and other processor based systems as the basic form of working memory within the system.
Although a variety of other different types of semiconductor memory that are available, dynamic RAM - DRAM is widely used in all forms of microprocessor and computer equipment.
Over the years, DRAM has been one of the most widely used memory technologies and is also in widespread use today.

## Slide 3: What is DRAM Technology
As the name DRAM, or dynamic random access memory, implies, this form of memory technology is a type of random access memory. It stores each bit of data on a small capacitor within the memory cell. The capacitor can be either charged or discharged and this provides the two states, ‘1’ or ‘0’ for the cell.
The advantage of a DRAM is the simplicity of the cell - it only requires a single transistor compared to around six in a typical static RAM, SRAM memory cell. N view of its simplicity, the costs of DRAM are much lower than those for SRAM, and they are able to provide much higher levels of memory density. However the DRAM has disadvantages as well, and as a result, most computers use both DRAM technology and SRAM, but in different areas.

## Slide 4: DRAM advantages and disadvantages
Advantages | Disadvantages
Very dense Low cost per bit Simple memory cell structure | Complex manufacturing process Data requires refreshing More complex external circuitry required (read and refresh periodically) Volatile memory Relatively slow operational speed

## Slide 5: DRAM applications & usage
Over a period of around 20 years, internal processor speeds have risen by a factor of around 40, yet in this time the speed of dynamic RAM technology has barely risen - they have seen a factor of two increase at the most.
The mismatch between processor and RAM is more pronounced for dynamic RAM, DRAM than for Static RAM, SRAM. This is because the dynamic RAM is optimized for low leakage and not for speed. However the cost of dynamic RAM is much lower and falling. As a result DRAM is used where cost efficient storage of large amounts of data is needed.

## Slide 6: DRAM applications & usage
The DRAM memory allows fast and dense memories to be made that are suitable for use with many processor and computer applications.
More recently other forms of DRAM, notably the SDRAM have improved the basic technology and enable greater levels of speed and density to be achieved.
As a result these newer forms of semiconductor memory are now more widely used that the more traditional DRAM chips.

## Slide 7: Static RAM (SRAM)
This form of semiconductor memory gains its name from the fact that data is held in there in a static fashion, and does not need to be dynamically updated as in the case of DRAM memory.
While the data in the SRAM memory does not need to be refreshed dynamically, it is still volatile, meaning that when the power is removed from the memory device, the data is not held, and will disappear.

## Slide 8: SRAM Memory basics
The data is held statically: This means that the data is held in the semiconductor memory without the need to be refreshed as long as the power is applied to the memory.
SRAM is a form of random access memory: A random access memory is one in which the locations in the semiconductor memory can be written to or read from in any order, regardless of the last memory location that was accessed.

## Slide 9: SRAM Memory basics…
The circuit for an individual SRAM memory cell comprises typically four transistors configured as two cross coupled inverters.
In this format the circuit has two stable states, and these equate to the logical "0" and "1" states.
In addition to the four transistors in the basic memory cell, and additional two transistors are required to control the access to the memory cell during the read and write operations.
This makes a total of six transistors, making what is termed a 6T memory cell. Sometimes further transistors are used to give either 8T or 10T memory cells.
These additional transistors are used for functions such as implementing additional ports in a register file, etc for the SRAM memory.

## Slide 10: SRAM memory applications
SRAM is a little more expensive than DRAM. However SRAM is faster and consumes less power especially when idle. In addition to this SRAM memory is easier to control than DRAM as the refresh cycles do not need to be taken into account, and in addition to this the way SRAM can be accessed is more exactly random access. A further advantage if SRAM is that it is more dense than DRAM.
As a result of these parameters, SRAM memory is used where speed or low power are considerations. Its higher density and less complicated structure also lend it to use in semiconductor memory scenarios where high capacity memory is used, as in the case of the working memory within computers.

## Slide 11: Synchronous Dynamic Random Access Memory
SDRAM, or Synchronous Dynamic Random Access Memory is a form of semiconductor memory can run at faster speeds than conventional DRAM and is therefore the use of SDRAM is becoming more widespread.
So effective is SDRAM, that it only took about four years after its introduction in 1996/7 before its use had exceeded that of DRAM in PCs because of its greater speed of operation.
Now SDRAM based memory is the major type of dynamic RAM used across the computing spectrum.

## Slide 12: SDRAM types and development
There are a number of different types of SDRAM that are available.
DDR SDRAM: This is the basic type of SDRAM that was first introduced. It has now been superseded by the other types below. It is referred to as single data rate SDRAM, or just SDRAM.
DDR SDRAM: DDR SDRAM gains its name from the fact that it is Double Data Rate SDRAM. This type of SDRAM provides data transfer at twice the speed of the traditional type of SDRAM memory. This is achieved by transferring data twice per cycle.
DDR2 SDRAM: DDR2 SDRAM can operate the external bus twice as fast as its predecessor and it was first introduced in 2003.
DDR3 SDRAM: DDR3 SDRAM is a further development of the double data rate type of SDRAM. It provides further improvements in overall performance and speed. As a result its use is becoming more widespread.
DDR4 SDRAM: This is a further type of SDRAM being developed and anticipated to be available in 2012.