## Slide 1: Unit II:ALU Design Lecture 12
Prepared By:
Avita Katal
Assistant Professor
Department of Virtualization
SoCSE

## Slide 2: Contents
Introduction
The Basic Computer
Instructions
Instruction Format
Processor Registers
Common Bus System
Timing and Signals

## Slide 3: 1. Introduction
Every different processor type has its own design (different registers, buses, microoperations, machine instructions, etc.)
Modern processor is a very complex device
It contains
  Many registers
  Multiple arithmetic units, for both integer and floating point calculations
  The ability to pipeline several consecutive instructions to speed execution
  Etc.
However, to understand how processors work, we will start with a simplified processor model
This is similar to what real processors were like ~25 years ago
M. Morris Mano introduces a simple processor model he calls the Basic Computer
We will use this to introduce processor organization and the relationship of the RTL model to the higher level computer processor

## Slide 4: 2. The Basic Computer
The Basic Computer has two components, a processor and memory
The memory has 4096 words in it
  4096 = 212, so it takes 12 bits to select a word in memory
Each word is 16 bits long
CPU
RAM
0
4095
0
15

## Slide 5: 3. Instructions
Program
  A sequence of (machine) instructions
(Machine) Instruction
  A group of bits that tell the computer to perform a specific operation (a sequence of micro-operation)
The instructions of a program, along with any needed data are stored in memory
The CPU reads the next instruction from memory
It is placed in an Instruction Register (IR)
Control circuitry in control unit then translates the instruction into the sequence of microoperations necessary to implement it

## Slide 6: 4. Instruction Format
A computer instruction is often divided into two parts
  An opcode (Operation Code) that specifies the operation for that instruction
  An address that specifies the registers and/or locations in memory to use for that operation
In the Basic Computer, since the memory contains 4096 (= 212) words, we needs 12 bit to specify which memory address this instruction will use
In the Basic Computer, bit 15 of the instruction specifies the addressing mode (0: direct addressing, 1: indirect addressing)
Since the memory words, and hence the instructions, are 16 bits long, that leaves 3 bits for the instruction’s opcode
Opcode
Address
Instruction Format
15
14
12
0
I
11
Addressing
mode

## Slide 7: Instruction Format contd…
The computer system presented here has three instruction formats.
Since instruction register is of 16 bits, the opcode part has 3 bits and interpretation of the remaining bits depends on the type of instruction. The three main types of instructions differ from each other depending on the value in opcode field.
  Memory reference instruction: It uses 12 bits to specify the address .Mode Bit, I=0 for Direct Addressing and 1 for Indirect Addressing.

## Slide 8: Instruction Format contd…
  Register reference instruction: In this opcode has a value 111 and 0 in the leftmost bit position. In this operand from the memory is not needed and operation is directly performed on the processor register specified. Since we assumed only one Processor Register (AC), in Register reference instruction the operand is implicit (contents of AC). For example Shift AC, Complement AC. The remaining 12 bits of the instruction register can be used to specify any one of the different register reference instructions.
  Input/Output: It has a value 111 in opcode and 1 in the leftmost bit of instruction register. The remaining 12 bits of the instruction register are used to specify any one of the Input/output instructions.
Thus, if the 3 bits of the code field contain a value 111 then it is either register reference or Input/Output. The control then checks the value in the first bit of instruction register, if it is 1 it is an Input/Output, if it is 0 then it is a register reference.

## Slide 9: Instruction Format contd…
Basic Computer Instruction Format
15 14
12 11
0
I
Opcode
Address
Memory-Reference Instructions (OP-code = 000 ~ 110)
Register-Reference Instructions (OP-code = 111, I = 0)
Input-Output Instructions (OP-code =111, I = 1)
15
12 11
0
Register operation
0 1 1 1
15
12 11
0
I/O operation
1 1 1 1

## Slide 10: 5. Processor Registers
A processor has many registers to hold instructions, addresses, data, etc.
The processor has a register, the Program Counter (PC) that holds the memory address of the next instruction to get
  Since the memory in the Basic Computer only has 4096 locations, the PC only needs 12 bits
In a direct or indirect addressing, the processor needs to keep track of what locations in memory it is addressing: The Address Register (AR) is used for this
  The AR is a 12 bit register in the Basic Computer
When an operand is found, using either direct or indirect addressing, it is placed in the Data Register (DR). The processor then uses this value as data for its operation
The Basic Computer has a single general purpose register – the Accumulator (AC)

## Slide 11: Processor Registers contd…
The significance of a general purpose register is that it can be referred to in instructions
  e.g. load AC with the contents of a specific memory location; store the contents of AC into a specified memory location
Often a processor will need a scratch register to store intermediate results or other temporary data; in the Basic Computer this is the Temporary Register (TR)
The Basic Computer uses a very simple model of input/output (I/O) operations
  Input devices are considered to send 8 bits of character data to the processor
  The processor can send 8 bits of character data to output devices
The Input Register (INPR) holds an 8 bit character gotten from an input device
The Output Register (OUTR) holds an 8 bit character to be send to an output device

## Slide 12: Basic Computer Registers
List of Registers
  DR 16 Data Register Holds memory operand
  AR 12 Address Register Holds address for memory
  AC 16 Accumulator Processor register
  IR 16 Instruction Register Holds instruction code
  PC 12 Program Counter Holds address of instruction
  TR 16 Temporary Register Holds temporary data
  INPR 8 Input Register Holds input character
  OUTR 8 Output Register Holds output character
Registers in the Basic Computer
11
0
PC
15
0
IR
15
0
TR
7
0
OUTR
15
0
DR
15
0
AC
11
0
AR
INPR
0
7
Memory
4096 x 16
CPU

## Slide 13: 6. Common Bus System
The registers in the Basic Computer are connected using a bus
This gives a savings in circuitry over complete connections between registers

## Slide 14: Common Bus System contd…
S2
S1
S0
Bus
Memory unit
4096 x 16
LD INR CLR
Address
Read
Write
AR
LD INR CLR
PC
LD INR CLR
DR
LD INR CLR
AC
ALU
E
INPR
IR
LD
LD INR CLR
TR
OUTR
LD
Clock
16-bit common bus
7
1
2
3
4
5
6

## Slide 15: Common Bus System contd…
Three control lines, S2, S1, and S0 control which register the bus selects as its input
Either one of the registers will have its load signal activated, or the memory will have its read signal activated
  Will determine where the data from the bus gets loaded
The 12-bit registers, AR and PC, have 0’s loaded onto the bus in the high order 4 bit positions
When the 8-bit register OUTR is loaded from the bus, the data comes from the low order 8 bits on the bus
0 0 0 x
0 0 1 AR
0 1 0 PC
0 1 1 DR
1 0 0 AC
1 0 1 IR
1 1 0 TR
1 1 1 Memory
S2 S1 S0 Register