## Slide 1: Unit II: ALU Design Lecture 15
Prepared By:
Avita Katal
Assistant Professor
Department of Virtualization
SoCS,UPES

## Slide 2: Contents
Instruction formats,
Timing and control
Instruction Sequencing & Instruction Cycles
Register Reference Instruction
Memory Reference Instruction
Input Output Instructions
Program Control
Performance and metrics.

## Slide 3: Instruction formats

## Slide 4: 1. 1 Introduction
Every different processor type has its own design (different registers, buses, microoperations, machine instructions, etc.)
Modern processor is a very complex device
It contains
  Many registers
  Multiple arithmetic units, for both integer and floating point calculations
  The ability to pipeline several consecutive instructions to speed execution
  Etc.
However, to understand how processors work, we will start with a simplified processor model
This is similar to what real processors were like ~25 years ago
M. Morris Mano introduces a simple processor model he calls the Basic Computer
We will use this to introduce processor organization and the relationship of the RTL model to the higher level computer processor

## Slide 5: 1.2. The Basic Computer
The Basic Computer has two components, a processor and memory
The memory has 4096 words in it
  4096 = 212, so it takes 12 bits to select a word in memory
Each word is 16 bits long
CPU
RAM
0
4095
0
15

## Slide 6: 1.3. Instructions
Program
  A sequence of (machine) instructions
(Machine) Instruction
  A group of bits that tell the computer to perform a specific operation (a sequence of micro-operation)
The instructions of a program, along with any needed data are stored in memory
The CPU reads the next instruction from memory
It is placed in an Instruction Register (IR)
Control circuitry in control unit then translates the instruction into the sequence of microoperations necessary to implement it

## Slide 7: 1.4. Instruction Format
A computer instruction is often divided into two parts
  An opcode (Operation Code) that specifies the operation for that instruction
  An address that specifies the registers and/or locations in memory to use for that operation
In the Basic Computer, since the memory contains 4096 (= 212) words, we needs 12 bit to specify which memory address this instruction will use
In the Basic Computer, bit 15 of the instruction specifies the addressing mode (0: direct addressing, 1: indirect addressing)
Since the memory words, and hence the instructions, are 16 bits long, that leaves 3 bits for the instruction’s opcode
Opcode
Address
Instruction Format
15
14
12
0
I
11
Addressing
mode

## Slide 8: 1.4. Instruction Format contd…
The computer system presented here has three instruction formats.
Since instruction register is of 16 bits, the opcode part has 3 bits and interpretation of the remaining bits depends on the type of instruction. The three main types of instructions differ from each other depending on the value in opcode field.
  Memory reference instruction: It uses 12 bits to specify the address .Mode Bit, I=0 for Direct Addressing and 1 for Indirect Addressing.

## Slide 9: 1.4.Instruction Format contd…
  Register reference instruction: In this opcode has a value 111 and 0 in the leftmost bit position. In this operand from the memory is not needed and operation is directly performed on the processor register specified.
    Since we assumed only one Processor Register (AC), in Register reference instruction the operand is implicit (contents of AC). For example Shift AC, Complement AC. The remaining 12 bits of the instruction register can be used to specify any one of the different register reference instructions.
  Input/Output: It has a value 111 in opcode and 1 in the leftmost bit of instruction register. The remaining 12 bits of the instruction register are used to specify any one of the Input/output instructions.
Thus, if the 3 bits of the code field contain a value 111 then it is either register reference or Input/Output. The control then checks the value in the first bit of instruction register, if it is 1 it is an Input/Output, if it is 0 then it is a register reference.

## Slide 10: 1.4. Instruction Format contd…
Basic Computer Instruction Format
15 14
12 11
0
I
Opcode
Address
Memory-Reference Instructions (OP-code = 000 ~ 110)
Register-Reference Instructions (OP-code = 111, I = 0)
Input-Output Instructions (OP-code =111, I = 1)
15
12 11
0
Register operation
0 1 1 1
15
12 11
0
I/O operation
1 1 1 1

## Slide 11: 1.4. Instruction Format contd…
PROCESSOR ORGANIZATION
In general, most processors are organized in one of 3 ways
  Single register (Accumulator) organization
    Basic Computer is a good example
    Accumulator is the only general purpose register
  General register organization
    Used by most modern computer processors
    Any of the registers can be used as the source or destination for computer operations
  Stack organization
    All operations are done using the hardware stack
    For example, an OR instruction will pop the two top elements from the stack, do a logical OR on them, and push the result on the stack

## Slide 12: 1.4. Instruction Format contd…
OP-code field - specifies the operation to be performed
Address field - designates memory address(es) or a processor register(s)
Mode field - determines how the address field is to be interpreted (to
get effective address or the operand)
The number of address fields in the instruction format depends on the internal organization of CPU
The three most common CPU organizations:
  Single accumulator organization:
  ADD X /* AC  AC + M[X] */
  General register organization:
  ADD R1, R2, R3 /* R1  R2 + R3 */
  ADD R1, R2 /* R1  R1 + R2 */
  MOV R1, R2 /* R1  R2 */
  ADD R1, X /* R1  R1 + M[X] */
  Stack organization:
  PUSH X /* TOS  M[X] */
  ADD
Instruction Fields

## Slide 13: 1.4. Instruction Format contd…
Three-Address Instructions
Program to evaluate X = (A + B) * (C + D) :
ADD R1, A, B /* R1  M[A] + M[B] */
ADD R2, C, D /* R2  M[C] + M[D] */
MUL X, R1, R2 /* M[X]  R1 * R2 */
- Results in short programs
- Instruction becomes long (many bits)
Two-Address Instructions
Program to evaluate X = (A + B) * (C + D) :
MOV R1, A /* R1  M[A] */
ADD R1, B /* R1  R1 + M[A] */
MOV R2, C /* R2  M[C] */
ADD R2, D /* R2  R2 + M[D] */
MUL R1, R2 /* R1  R1 * R2 */
MOV X, R1 /* M[X]  R1 */

## Slide 14: 1.4. Instruction Format contd…
One-Address Instructions
- Use an implied AC register for all data manipulation
- Program to evaluate X = (A + B) * (C + D) :
LOAD A /* AC  M[A] */
ADD B /* AC  AC + M[B] */
STORE T /* M[T]  AC */
LOAD C /* AC  M[C] */
ADD D /* AC  AC + M[D] */
MUL T /* AC  AC * M[T] */
STORE X /* M[X]  AC */
Zero-Address Instructions
- Can be found in a stack-organized computer
- Program to evaluate X = (A + B) * (C + D) :
PUSH A /* TOS  A */
PUSH B /* TOS  B */
ADD /* TOS  (A + B) */
PUSH C /* TOS  C */
PUSH D /* TOS  D */
ADD /* TOS  (C + D) */
MUL /* TOS  (C + D) * (A + B) */
POP X /* M[X]  TOS */

## Slide 15: 5. Processor Registers
A processor has many registers to hold instructions, addresses, data, etc.
The processor has a register, the Program Counter (PC) that holds the memory address of the next instruction to get
  Since the memory in the Basic Computer only has 4096 locations, the PC only needs 12 bits
In a direct or indirect addressing, the processor needs to keep track of what locations in memory it is addressing: The Address Register (AR) is used for this
  The AR is a 12 bit register in the Basic Computer
When an operand is found, using either direct or indirect addressing, it is placed in the Data Register (DR). The processor then uses this value as data for its operation
The Basic Computer has a single general purpose register – the Accumulator (AC)

## Slide 16: 2. Timing and control

## Slide 17: 2. Timing and control
Before getting to timing and control, we need to revise some topics like
Computer Registers
Common Bus System

## Slide 18: 2.1 Processor Registers contd…
The significance of a general purpose register is that it can be referred to in instructions
  e.g. load AC with the contents of a specific memory location; store the contents of AC into a specified memory location
Often a processor will need a scratch register to store intermediate results or other temporary data; in the Basic Computer this is the Temporary Register (TR)
The Basic Computer uses a very simple model of input/output (I/O) operations
  Input devices are considered to send 8 bits of character data to the processor
  The processor can send 8 bits of character data to output devices
The Input Register (INPR) holds an 8 bit character gotten from an input device
The Output Register (OUTR) holds an 8 bit character to be send to an output device

## Slide 19: 2.1 Processor Registers contd…
List of Registers
  DR 16 Data Register Holds memory operand
  AR 12 Address Register Holds address for memory
  AC 16 Accumulator Processor register
  IR 16 Instruction Register Holds instruction code
  PC 12 Program Counter Holds address of instruction
  TR 16 Temporary Register Holds temporary data
  INPR 8 Input Register Holds input character
  OUTR 8 Output Register Holds output character
Registers in the Basic Computer
11
0
PC
15
0
IR
15
0
TR
7
0
OUTR
15
0
DR
15
0
AC
11
0
AR
INPR
0
7
Memory
4096 x 16
CPU

## Slide 20: 2. 2 Common Bus System
The registers in the Basic Computer are connected using a bus
This gives a savings in circuitry over complete connections between registers

## Slide 21: 2. 2 Common Bus System contd…
S2
S1
S0
Bus
Memory unit
4096 x 16
LD INR CLR
Address
Read
Write
AR
LD INR CLR
PC
LD INR CLR
DR
LD INR CLR
AC
ALU
E
INPR
IR
LD
LD INR CLR
TR
OUTR
LD
Clock
16-bit common bus
7
1
2
3
4
5
6

## Slide 22: 2. 2 Common Bus System contd…
Three control lines, S2, S1, and S0 control which register the bus selects as its input
Either one of the registers will have its load signal activated, or the memory will have its read signal activated
  Will determine where the data from the bus gets loaded
The 12-bit registers, AR and PC, have 0’s loaded onto the bus in the high order 4 bit positions
When the 8-bit register OUTR is loaded from the bus, the data comes from the low order 8 bits on the bus
0 0 0 x
0 0 1 AR
0 1 0 PC
0 1 1 DR
1 0 0 AC
1 0 1 IR
1 1 0 TR
1 1 1 Memory
S2 S1 S0 Register

## Slide 23: 2.3. Timing and Control
Control unit of Basic Computer
Instruction register (IR)
15
14 13 12
11 - 0
3 x 8
decoder
7 6 5 4 3 2 1 0
I
D
0
15 14 . . . . 2 1 0
4 x 16
decoder
4-bit
sequence
counter
(SC)
Increment (INR)
Clear (CLR)
Clock
Other inputs
Control
signals
D
T
T
7
15
0
Combinational
Control
logic

## Slide 24: 2.4. Timing Signals
- Generated by 4-bit sequence counter and 416 decoder
- The SC can be incremented or cleared.
- Example: T0, T1, T2, T3, T4, T0, T1, . . .
Assume: At time T4, SC is cleared to 0 if decoder output D3 is active.
D3T4: SC  0

## Slide 25: 3. Instruction Sequencing and instruction cycle

## Slide 26: 3.1. Instruction Cycle
In Basic Computer, a machine instruction is executed in the following cycle:
  Fetch an instruction from memory
  Decode the instruction
  Read the effective address from memory if the instruction has an indirect address
  Execute the instruction
After an instruction is executed, the cycle starts again at step 1, for the next instruction
Note: Every different processor has its own (different) instruction cycle

## Slide 27: 3.1.1 Fetch and Decode
• Fetch and Decode
T0: AR PC (S0S1S2=010, T0=1)
T1: IR  M [AR], PC  PC + 1 (S0S1S2=111, T1=1)
T2: D0, . . . , D7  Decode IR(12-14), AR  IR(0-11), I  IR(15)
S2
S1
S0
Bus
7
Memory
unit
Address
Read
AR
LD
PC
INR
IR
LD
Clock
1
2
5
Common bus
T1
T0

## Slide 28: 3.1.2. Determine the Type of the Instruction
= 0 (direct)
D'7IT3: AR M[AR]
D'7I'T3: Nothing
D7I'T3: Execute a register-reference instr.
D7IT3: Execute an input-output instr.
Start
SC  0
AR

PC
T0
IR

M[AR],
PC

PC + 1
T1
AR

IR(0-11),
I

IR(15)
Decode Opcode in IR(12-14),
T2
D7
= 0 (Memory-reference)
(Register or I/O) = 1
I
I
Execute
register-reference
instruction
SC

0
Execute
input-output
instruction
SC

0
M[AR]

AR
Nothing
= 0 (register)
(I/O) = 1
(indirect) = 1
T3
T3
T3
T3
Execute
memory-reference
instruction
SC

0
T4

## Slide 29: 4. Register reference Instructions

## Slide 30: 4. Register Reference Instruction
r = D7 IT3 => Register Reference Instruction
Bi = IR(i) , i=0,1,2,...,11
- D7 = 1, I = 0
- Register Ref. Instr. is specified in b0 ~ b11 of IR
- Execution starts with timing signal T3
Register Reference Instructions are identified when
r: SC  0
CLA rB11: AC  0
CLE rB10: E  0
CMA rB9: AC  AC’
CME rB8: E  E’
CIR rB7: AC  shr AC, AC(15)  E, E  AC(0)
CIL rB6: AC  shl AC, AC(0)  E, E  AC(15)
INC rB5: AC  AC + 1
SPA rB4: if (AC(15) = 0) then (PC  PC+1)
SNA rB3: if (AC(15) = 1) then (PC  PC+1)
SZA rB2: if (AC = 0) then (PC  PC+1)
SZE rB1: if (E = 0) then (PC  PC+1)
HLT rB0: S  0 (S is a start-stop flip-flop)

## Slide 31: 4. Register Reference Instruction contd…
Register-reference instructions are recognized by the control when D7 = 1 and I = 0. These instructions use bits 0 through 11 of the instruction code to specify one of 12 instructions.
These 12 bits are available in IR(0-11).
These instructions are executed with the clock transition associated with timing variable T3• Each control function needs the Boolean relation D7I'T3, which we designate for convenience by the symbol r.
The control function is distinguished by one of the bits in IR(0-11). By assigning the symbol B, to bit i of IR, all control functions can be simply denoted by rBi

## Slide 32: 5. Memory Reference Instructions

## Slide 33: 5. Memory Reference Instruction
AND to AC
D0T4: DR  M[AR] Read operand
D0T5: AC  AC  DR, SC  0 AND with AC
ADD to AC
D1T4: DR  M[AR] Read operand
D1T5: AC  AC + DR, E  Cout, SC  0 Add to AC and store carry in E
- The effective address of the instruction is in AR and was placed there during
timing signal T2 when I = 0, or during timing signal T3 when I = 1
- Memory cycle is assumed to be short enough to complete in a CPU cycle
- The execution of MR instruction starts with T4
Symbol
Operation
Decoder
Symbolic Description
AND D0 AC  AC  M[AR]
ADD D1 AC  AC + M[AR], E  Cout
LDA D2 AC  M[AR]
STA D3 M[AR]  AC
BUN D4 PC  AR
BSA D5 M[AR]  PC, PC  AR + 1
ISZ D6 M[AR]  M[AR] + 1, if M[AR] + 1 = 0 then PC  PC+1

## Slide 34: 5 Memory Reference Instruction contd…
Memory, PC after execution
21
0
BSA
135
Next instruction
Subroutine
20
PC = 21
AR = 135
136
1
BUN
135
Memory, PC, AR at time T4
0
BSA
135
Next instruction
Subroutine
20
21
135
PC = 136
1
BUN
135
Memory
Memory
LDA: Load to AC
D2T4: DR  M[AR]
D2T5: AC  DR, SC  0
STA: Store AC
D3T4: M[AR]  AC, SC  0
BUN: Branch Unconditionally
D4T4: PC  AR, SC  0
BSA: Branch and Save Return Address
M[AR]  PC, PC  AR + 1

## Slide 35: 5. Memory Reference Instruction contd…
BSA:
D5T4: M[AR]  PC, AR  AR + 1
D5T5: PC  AR, SC  0
ISZ: Increment and Skip-if-Zero
D6T4: DR  M[AR]
D6T5: DR  DR + 1
D6T4: M[AR]  DR, if (DR = 0) then (PC  PC + 1), SC  0

## Slide 36: 5. Memory Reference Instruction contd…
Memory-reference instruction
DR  M[AR]
DR  M[AR]
DR  M[AR]
M[AR]  AC
SC  0
AND
ADD
LDA
STA
AC  AC DR
SC  0
AC  AC + DR
E  Cout
SC  0
AC  DR
SC  0
D T
0
4
D T
1
4
D T
2
4
D T
3
4
D T
0
5
D T
1
5
D T
2
5
PC  AR
SC  0
M[AR]  PC
AR  AR + 1
DR  M[AR]
BUN
BSA
ISZ
D T
4
4
D T
5
4
D T
6
4
DR  DR + 1
D T
5
5
D T
6
5
PC  AR
SC  0
M[AR]  DR
If (DR = 0)
then (PC  PC + 1)
SC  0
D T
6
6


## Slide 37: 6. Input Output Instructions

## Slide 38: 6. Input Output Instruction
Before studying Input Output Instructions, the third type of instructions, we need to understand the working of I/O devices.
We would be covering
  Input-Output and Interrupt
  Program Controlled Data Transfer
  Input output Instructions in this section

## Slide 39: 6.1. Input-Output and Interrupt
Input-Output Configuration
INPR Input register - 8 bits
OUTR Output register - 8 bits
FGI Input flag - 1 bit
FGO Output flag - 1 bit
IEN Interrupt enable - 1 bit
- The terminal sends and receives serial information
- The serial info. from the keyboard is shifted into INPR
- The serial info. for the printer is stored in the OUTR
- INPR and OUTR communicate with the terminal serially and with the AC in parallel.
- The flags are needed to synchronize the timing difference between I/O device and the computer
A Terminal with a keyboard and a Printer
Input-output
terminal
Serial
communication
interface
Computer
registers and
flip-flops
Printer
Keyboard
Receiver
interface
Transmitter
interface
FGO
OUTR
AC
INPR
FGI
Serial Communications Path
Parallel Communications Path

## Slide 40: 6.2. Program Controlled Data Transfer
loop: If FGI = 1 goto loop
INPR  new data, FGI  1
loop: If FGO = 1 goto loop
consume OUTR, FGO  1
-- CPU -- -- I/O Device --
/* Input */ /* Initially FGI = 0 */
loop: If FGI = 0 goto loop
AC  INPR, FGI  0
/* Output */ /* Initially FGO = 1 */
loop: If FGO = 0 goto loop
OUTR  AC, FGO  0
Start Input
FGI  0
FGI=0
AC  INPR
More
Character
END
Start Output
FGO  0
FGO=0
More
Character
END
OUTR  AC
AC  Data
yes
no
yes
no
FGI=0
FGO=1
yes
yes
no
no

## Slide 41: 6.3. Input Output Instructions
D7IT3 = p
IR(i) = Bi, i = 6, …, 11
p: SC  0 Clear SC
INP pB11: AC(0-7)  INPR, FGI  0 Input char. to AC
OUT pB10: OUTR  AC(0-7), FGO  0 Output char. from AC
SKI pB9: if(FGI = 1) then (PC  PC + 1) Skip on input flag
SKO pB8: if(FGO = 1) then (PC  PC + 1) Skip on output flag
ION pB7: IEN  1 Interrupt enable on
IOF pB6: IEN  0 Interrupt enable off

## Slide 42: 7. Program Conrol

## Slide 43: 7.1 FLAG, PROCESSOR STATUS WORD
In Basic Computer, the processor had several (status) flags – 1 bit value that indicated various information about the processor’s state – E, FGI, FGO, I, IEN, R
In some processors, flags like these are often combined into a register – the processor status register (PSR); sometimes called a processor status word (PSW)
Common flags in PSW are
  C (Carry): Set to 1 if the carry out of the ALU is 1
  S (Sign): The MSB bit of the ALU’s output
  Z (Zero): Set to 1 if the ALU’s output is all 0’s
  V (Overflow): Set to 1 if there is an overflow
Status Flag Circuit
c7
c8
A B
8 8
8-bit ALU
V Z S C
F7
F7 - F0
8
F
Check for
zero output

## Slide 44: 7.2. PROGRAM CONTROL INSTRUCTIONS
PC
+1
In-Line Sequencing (Next instruction is fetched from the next adjacent location in the memory)
Address from other source; Current Instruction, Stack, etc; Branch, Conditional Branch, Subroutine, etc
Program Control Instructions
Name Mnemonic
Branch BR
Jump JMP
Skip SKP
Call CALL
Return RTN
Compare(by  ) CMP
Test(by AND) TST
* CMP and TST instructions do not retain their
results of operations (  and AND, respectively).
They only set or clear certain Flags.

## Slide 45: 7.3. CONDITIONAL BRANCH INSTRUCTIONS
BZ Branch if zero Z = 1
BNZ Branch if not zero Z = 0
BC Branch if carry C = 1
BNC Branch if no carry C = 0
BP Branch if plus S = 0
BM Branch if minus S = 1
BV Branch if overflow V = 1
BNV Branch if no overflow V = 0
BHI Branch if higher A > B
BHE Branch if higher or equal A  B
BLO Branch if lower A < B
BLOE Branch if lower or equal A  B
BE Branch if equal A = B
BNE Branch if not equal A  B
BGT Branch if greater than A > B
BGE Branch if greater or equal A  B
BLT Branch if less than A < B
BLE Branch if less or equal A  B
BE Branch if equal A = B
BNE Branch if not equal A  B
Unsigned compare conditions (A - B)
Signed compare conditions (A - B)
Mnemonic Branch condition Tested condition

## Slide 46: 7.4. SUBROUTINE CALL AND RETURN
Call subroutine
Jump to subroutine
Branch to subroutine
Branch and save return address
Fixed Location in the subroutine (Memory)
Fixed Location in memory
In a processor Register
In memory stack
- most efficient way
Subroutine Call
Two Most Important Operations are Implied;
* Branch to the beginning of the Subroutine
- Same as the Branch or Conditional Branch
* Save the Return Address to get the address
of the location in the Calling Program upon
exit from the Subroutine
Locations for storing Return Address
CALL
SP  SP - 1
M[SP]  PC
PC  EA
RTN
PC  M[SP]
SP  SP + 1

## Slide 47: 7.5. PROGRAM INTERRUPT
Types of Interrupts
External interrupts
External Interrupts initiated from the outside of CPU and Memory
- I/O Device → Data transfer request or Data transfer complete
- Timing Device → Timeout
- Power Failure
- Operator
Internal interrupts (traps)
Internal Interrupts are caused by the currently running program
- Register, Stack Overflow
- Divide by zero
- OP-code Violation
- Protection Violation
Software Interrupts
Both External and Internal Interrupts are initiated by the computer HW.
Software Interrupts are initiated by the executing an instruction.
- Supervisor Call → Switching from a user mode to the supervisor mode
→ Allows to execute a certain class of operations
which are not allowed in the user mode

## Slide 48: 7.5.1 INTERRUPT PROCEDURE
  The interrupt is usually initiated by an internal or an external signal rather
  than from the execution of an instruction (except for the software interrupt)
  The address of the interrupt service program is determined by the hardware
  rather than from the address field of an instruction
  An interrupt procedure usually stores all the information necessary to define
  the state of CPU rather than storing only the PC.
  The state of the CPU is determined from;
  Content of the PC
  Content of all processor registers
  Content of status bits
  Many ways of saving the CPU state depending on the CPU architectures
Interrupt Procedure and Subroutine Call

## Slide 49: 8. Performance and Metrics

## Slide 50: 8.1. Computer Performance Factors
The performance of a computer is measured by the amount of time taken by the computer to execute a program.
For two computers operating at the same clock rate, the execution time for ADD instruction can be different if they have different internal organizations.
Also, for a given computer , the time taken for different instructions are not equal. MULTIPLY will take more time than ADD instruction
The type of instruction and number of instructions executed by the CPU while running a program decides the time taken by a computer for the program
Tp = Nie x CPI
F
Where Nie is the number of instructions, CPI is the average number of Clock Cycles needed for an instruction and F is the clock frequency

## Slide 51: 8.1. Computer Performance Factors contd…
Thus , reducing Nie and CPI and increasing F can reduce the program execution time
Reducing Nie involves having less instructions in the compiled program which is related to compiler efficiency and instruction set.
Reducing CPI involves better CPU design to shorten instruction cycle and increasing F involves higher clock frequency which depends on technology.

## Slide 52: 8.2. System Performance measurement
For a given computer, there are two simple measurements that give us an idea about its performance:
Response Time: Time taken by the computer to execute a given program, from the start to the end of the program .The response time for a program is different for different computers.
Throughput: Work done (no. of programs executed) by the computer during a given period of time
Execution time for B/Execution time for A =n
In other words, n =Performance of A/Performance of B

## Slide 53: 8.2.1 MIPS
Millions of instructions executed Per second was commonly used to indicate the speed of a computer.
Since instruction cycle time is different for different instructions, the MIPS value will differ for different instructions mix in the program
Hence, MIPS value of a computer gives only a rough idea about the system performance.

## Slide 54: 8.2.2 Benchmark Programs
These are the evaluation programs which are used to compare the performance of different computers.
The time taken by a computer to execute benchmark program is taken as a measure of its performance.
The ability of a benchmark program to give reasonably accurate information about the performance of a computer depends on the instruction mix used in the program.

## Slide 55: 8.2.3. Benchmark Suite
It is a collection of different types of benchmark programs.
Running a benchmark suite on a computer gives a reasonably good idea about the performance of a computer.
Since there are variety of programs in a suite the weaknesses of one program are compensated by the strength of other program.

## Slide 56: 8.2.4. SPEC Rating
The System Performance Evaluation Corporation (SPEC) is a non- profit organization dedicated for performance evaluation.
It selects typical application programs for different application areas and publishes the performance results for important commercial computers.
The performance of other computers are rated as relative measure of the standard computer.

## Slide 57: 8.3. High Performance Architecture
Two approaches for enhancing the performance of a processor:
1. Increasing the clock frequency
2. Increasing the number of operations performed during each clock cycle.
Increasing the clock frequency depends upon IC fabrication process. For performing more operations per clock cycle:
1. Providing multiple functional units in a single processor chip.
2. Executing multiple instructions concurrently by fully loading the functional units.

## Slide 58: 8.3.1 Reducing Memory Access Time
Cache Memory
Having a small and fast memory between CPU and RAM in which certain contents of RAM are temporarily stored in advance.
Being fast CPU fetches instruction or Operand in shorter time than Main Memory access time
Memory Interleaving:
Organizing the main memory into two independent banks with one containing all odd addresses and other containing all even addresses is k/a memory interleaving.
When CPU is accessing more than one consecutive memory locations, both odd and even banks can perform simultaneous read/write operations. This effectively cuts the access time by half.

## Slide 59: 8.3.2. Reducing Instruction Decode Time
Pre-Decode
The time taken for decoding depends on the h/w circuit technology. It can overlap with the execution time of the previous instruction if it has already been fetched.
Instruction pipelining
CPU can be divided into different sections so that each stage of an instruction cycle can be done by an independent section. All sections can work simultaneously for different instructions. This technique is known as Instruction Pipelining.
Superscalar architecture
If more than one adder is available in a CPU, all adders can work simultaneously for consecutive instructions. The technique is known as superscalar architecture. Generally two or more pipelines are present in a single CPU.

## Slide 60: 8.4. Instruction Set
There are two popular architectural standards for CPU design:
Complex Instruction Set Computing
Reduced Instruction Set Computing

## Slide 61: 8.4.1 Differences
S. No | RISC | CISC
1 | RISC stands for Reduced Instruction Set Computer | CISC stands for Complex Instruction Set Computer
2 | RISC processors have simple instructions taking about one clock cycle. The average Clock cycles Per Instruction(CPI) of a RISC processor is 1.5 | CISC processors have complex instructions that take up multiple clock cycles for execution. The average Clock cycles Per Instruction of a CISC processor is between 2 and 15
3 | There are hardly any instructions that refer memory. | Most of the instructions refer memory
4 | RISC processors have a fixed instruction format | CISC processors have variable instruction format.
5 | The instruction set is reduced i.e. it has only few instructions in the instruction set. Many of these instructions are very primitive. | The instruction set has a variety of different instructions that can be used for complex operations.
6 | RISC has fewer addressing modes and most of the instructions in the instruction set have register to register addressing mode. | CISC has many different addressing modes and can thus be used to represent higher level programming language statements more efficient

## Slide 62: 8.4.1 Differences contd…
Sl. No | RISC | CISC
7 | Complex addressing modes are synthesized using software. | CISC already supports complex addressing modes
8 | Multiple register sets are present | Only has a single register set
9 | RISC processors are highly pipelined | They are normally not pipelined or less pipelined
10 | The complexity of RISC lies in the compiler that executes the program. | The complexity lies in the micro program
11 | The most common RISC microprocessors are Alpha, ARC, ARM, AVR, MIPS, PA-RISC, PIC, Power Architecture, and SPARC. | Examples of CISC processors are the System/360, VAX, PDP-11, Motorola 68000 family, AMD and Intel x86 CPUs.

## Slide 63: Thanks…