## Slide 1: Unit II:ALU Design Lecture 13
Prepared by:
AVITA KATAL
Assistant Professor
Department of Virtualization
SoCSE

## Slide 2: Contents
Registers
General register Organization
Register Stack organization
Memory stack organization
Reverse polish Notation
Instruction Format
Three and Two Address Instruction
One and Zero Address Instruction

## Slide 3: 1. Registers
In Basic Computer, there is only one general purpose register, the Accumulator (AC)
In modern CPUs, there are many general purpose registers
It is advantageous to have many registers
  Transfer between registers within the processor are relatively fast
  Going “off the processor” to access memory is much slower
How many registers will be the best ?

## Slide 4: 2. General Register Organization
MUX
SELA
{
MUX
}
SELB
ALU
OPR
R1
R2
R3
R4
R5
R6
R7
Input
3 x 8
decoder
SELD
Load
(7 lines)
Output
A bus
B bus
Clock

## Slide 5: General Register Organization contd…
The control unit
Directs the information flow through ALU by
- Selecting various Components in the system
- Selecting the Function of ALU
Example: R1  R2 + R3
[1] MUX A selector (SELA): BUS A  R2
[2] MUX B selector (SELB): BUS B  R3
[3] ALU operation selector (OPR): ALU to ADD
[4] Decoder destination selector (SELD): R1  Out Bus
Control Word
Encoding of register selection fields
  Binary
  Code SELA SELB SELD
  000 Input Input None
  001 R1 R1 R1
  010 R2 R2 R2
  011 R3 R3 R3
  100 R4 R4 R4
  101 R5 R5 R5
  110 R6 R6 R6
  111 R7 R7 R7
SELA
SELB
SELD
OPR
3
3
3
5

## Slide 6: General Register Organization contd…
Encoding of ALU operations
OPR
Select Operation Symbol
00000 Transfer A TSFA
00001 Increment A INCA
00010 ADD A + B ADD
00101 Subtract A - B SUB
00110 Decrement A DECA
01000 AND A and B AND
01010 OR A and B OR
01100 XOR A and B XOR
01110 Complement A COMA
10000 Shift right A SHRA
11000 Shift left A SHLA
Examples of ALU Microoperations
Symbolic Designation
Microoperation SELA SELB SELD OPR Control Word
  R1  R2  R3 R2 R3 R1 SUB 010 011 001 00101
  R4  R4  R5 R4 R5 R4 OR 100 101 100 01010
  R6  R6 + 1 R6 - R6 INCA 110 000 110 00001
  R7  R1 R1 - R7 TSFA 001 000 111 00000
  Output  R2 R2 - None TSFA 010 000 000 00000
  Output  Input Input - None TSFA 000 000 000 00000
  R4  shl R4 R4 - R4 SHLA 100 000 100 11000
  R5  0 R5 R5 R5 XOR 101 101 101 01100

## Slide 7: 3. Register Stack Organization
Register Stack
Push, Pop operations
/* Initially, SP = 0, EMPTY = 1, FULL = 0 */
PUSH
POP
  SP  SP + 1 DR  M[SP]
  M[SP]  DR SP  SP  1
  If (SP = 0) then (FULL  1) If (SP = 0) then (EMPTY  1)
  EMPTY  0 FULL  0
Stack
- Very useful feature for nested subroutines, nested interrupt services
- Also efficient for arithmetic expression evaluation
- Storage which can be accessed in LIFO
- Pointer: SP
- Only PUSH and POP operations are applicable
A
B
C
0
1
2
3
4
63
Address
FULL
EMPTY
SP
DR
Flags
Stack pointer
stack
6 bits

## Slide 8: 4. Memory Stack Organization
- A portion of memory is used as a stack with a
processor register as a stack pointer
- PUSH: SP  SP - 1
  M[SP]  DR
- POP: DR  M[SP]
  SP  SP + 1
Memory with Program, Data,
and Stack Segments
4001
4000
3999
3998
3997
3000
Data
(operands)
Program
(instructions)
1000
PC
AR
SP
stack
Stack grows
In this direction
- Most computers do not provide hardware to check stack overflow (full
stack) or underflow (empty stack)  must be done in software

## Slide 9: 5. Reverse Polish Notation
A + B Infix notation
+ A B Prefix or Polish notation
A B + Postfix or reverse Polish notation
- The reverse Polish notation is very suitable for stack manipulation
Evaluation of Arithmetic Expressions
Any arithmetic expression can be expressed in parenthesis-free
Polish notation, including reverse Polish notation
(3 * 4) + (5 * 6)  3 4 * 5 6 * +
Arithmetic Expressions: A + B
3
3
12
12
12
12
42
4
5
5
6
30
3
4
*
5
6
*
+

## Slide 10: 6. Processor organization
In general, most processors are organized in one of 3 ways
  Single register (Accumulator) organization
    Basic Computer is a good example
    Accumulator is the only general purpose register
  General register organization
    Used by most modern computer processors
    Any of the registers can be used as the source or destination for computer operations
  Stack organization
    All operations are done using the hardware stack
    For example, an OR instruction will pop the two top elements from the stack, do a logical OR on them, and push the result on the stack

## Slide 11: 7. Instruction Format
OP-code field - specifies the operation to be performed
Address field - designates memory address(es) or a processor register(s)
Mode field - determines how the address field is to be interpreted (to
get effective address or the operand)
The number of address fields in the instruction format
depends on the internal organization of CPU
The three most common CPU organizations:
  Single accumulator organization:
  ADD X /* AC  AC + M[X] */
  General register organization:
  ADD R1, R2, R3 /* R1  R2 + R3 */
  ADD R1, R2 /* R1  R1 + R2 */
  MOV R1, R2 /* R1  R2 */
  ADD R1, X /* R1  R1 + M[X] */
  Stack organization:
  PUSH X /* TOS  M[X] */
  ADD
Instruction Fields

## Slide 12: 8. Three and Two address Instruction
Three-Address Instructions
Program to evaluate X = (A + B) * (C + D) :
ADD R1, A, B /* R1  M[A] + M[B] */
ADD R2, C, D /* R2  M[C] + M[D] */
MUL X, R1, R2 /* M[X]  R1 * R2 */
- Results in short programs
- Instruction becomes long (many bits)
Two-Address Instructions
Program to evaluate X = (A + B) * (C + D) :
MOV R1, A /* R1  M[A] */
ADD R1, B /* R1  R1 + M[A] */
MOV R2, C /* R2  M[C] */
ADD R2, D /* R2  R2 + M[D] */
MUL R1, R2 /* R1  R1 * R2 */
MOV X, R1 /* M[X]  R1 */

## Slide 13: 9. One and Zero address Instruction
One-Address Instructions
- Use an implied AC register for all data manipulation
- Program to evaluate X = (A + B) * (C + D) :
LOAD A /* AC  M[A] */
ADD B /* AC  AC + M[B] */
STORE T /* M[T]  AC */
LOAD C /* AC  M[C] */
ADD D /* AC  AC + M[D] */
MUL T /* AC  AC * M[T] */
STORE X /* M[X]  AC */
Zero-Address Instructions
- Can be found in a stack-organized computer
- Program to evaluate X = (A + B) * (C + D) :
PUSH A /* TOS  A */
PUSH B /* TOS  B */
ADD /* TOS  (A + B) */
PUSH C /* TOS  C */
PUSH D /* TOS  D */
ADD /* TOS  (C + D) */
MUL /* TOS  (C + D) * (A + B) */
POP X /* M[X]  TOS */